## Slide 1
Assiniboine River
Water Demand and Water Supply Studies
Prepared by:
Bob Harrison , P. Eng. and Abul Kashem, P. Eng.
Surface Water Management Section
Manitoba Conservation and Water Stewardship
PRAC Forum
Regina, February 15-16, 2012

## Slide 2: Outline
Background
Purpose
Socio-economic factors
Climate change Projections
Studies
  Water Demand
  Water Supply

## Slide 3
Manitoba portion of Assiniboine River is a major source of water for municipal agricultural, industrial, La Salle Diversion, and recreational water uses.
Background

## Slide 4
Shellmouth Dam
Manitoba flows are regulated by Shellmouth Dam a multi-purpose facility operated for flood control and water supply.
Assiniboine River / Shellmouth Reservoir system firm yield is about 112,500 acre-ft. (with 16,000 acre-ft potentially reserved for instream flows).
Current 82,000 acre-ft. is allocated
Irrigation largest use (about 25%).
Background

## Slide 5
Water demand study was to project future water uses with and without climate change (Genivar).
Water supply study was to assess the potential effects of climate change on surface water supply and soil moisture (Stantec).
Purpose

## Slide 6
6
  Future: stable agriculture based economy
  Growth rate: medium 0.66% / year based on 1991 to 2006.
Socio-economic Factors

## Slide 7
Provincial Attributes:
  Weathered global recession
  Diversified economy
  Strong resource sector led by agriculture, hydro and mining.
  Strong immigrant program.
  Comparatively inexpensive and renewable energy sources – hydro, wind.
.
Socio-economic Factors

## Slide 8
Study Area Attributes:
    Well serviced, affordable, welcoming communities.
    Water availability for domestic, municipal industrial and agricultural use.
    Superior soils within the lower Basin.
    Location along Asia-Pacific Trade Corridor.
    Ready access to American mid-west markets.
    Well positioned to respond to global food shortages.
.
Socio-economic Factors

## Slide 9
Future Climate Change Projection
Temperatures
Expected to increase
  Winter: between 2-6°C
  Spring: between 1-4°C.
  Summer: between 1.5-5°C.
  Fall: between 2-5°C.
Precipitation
  Reductions are predicted for the summer season, with reductions growing with time for this season.
  Increases are predicted for the other three seasons, with the largest increases in the spring.

## Slide 10
Future Climate Change Projection
CRCM model domain
45X45km
General
More frost-free days are anticipated.
Earlier seeding opportunities by approximately two to three weeks.
Increased potential for spring flooding.
Increased potential for summer droughts.

## Slide 11
Review of existing water use/demand,
Conduct a “visioning process”.
Quantified the sectoral water demand for the Assiniboine River for the periods 2010, 2020, 2050 and 2080 through an analysis of population, economic growth, agricultural trends and climate change.
Report prepared on projected demands.
Water Demand Study

## Slide 12
Water Demand Study

## Slide 13
Water demand will continue to increase over the study period, and may exceed the firm annual yield.
Climate change is predicted to strongly affect water demand from the river. In scenarios run without climate change, water demand exceeds available yield by 2080.
Under the climate change scenarios examined, irrigation demand will be dramatically higher than planning accounts for by 2050.
More study is needed to determine the potential for peak usage in months when river flows are low.
Conclusions: Water Demand Study

## Slide 14
14
The instream ecological needs of the river are not well quantified and should be studied further.
Accessing easy to use climate projection data was a challenge. A region-specific climate projection data inventory is currently not available or accessible to the public, but if available would be a very important resource for assessors and in adaptation planning efforts.
Conclusions: Water Demand Study

## Slide 15
    Modelled the hydrologic aspects of climate change based on the Canadian Regional Climate Model (CRM) run “aet”.
    Used DHI MIKE-SHE computer model.
    Model calibrated and verified for the periods from 1961 to 1990 and 1991 to 2003 respectively through comparison of unregulated simulated and observed flows
Water Supply Study
    Compared historical data to modelled climate change scenario data.
    Cautionary Note: There is breath of uncertainty as
    only one CRM model run (aet) assessed.

## Slide 16
Reviewed the natural mean monthly historical streamflow variability at Headingley for three periods.
Compared future streamflow scenarios for: 2011-2040, 2041-2070, 2071-2099 to historic .
Surface Water
Future scenarios are within historical natural variation, and no significant trend is apparent.
ASSINIBOINE RIVER ANNUAL FLOW DURATION CURVE
% of time less than

## Slide 17
Manitoba basin: soil moisture would not decline significantly until a later 21th century (2071).
Souris River basin: soil moisture will generally become drier in future, the lowest value in the latter third of the 21st century.
Qu’Appelle River Sub-basin: soil moisture will decrease in the first third and the last third and increase in the second third of the 21st century.
Soil Moisture
% of time less than
% of time less than
% of time less than

## Slide 18
Predicted warmer summers and falls leading to higher evapotranspiration and a resulting decline in soil moisture. The greatest decline is predicted to take place after 2070.
Predicted lower summer and fall soil moisture with no change in the spring soil moisture.
Historic year to year and decade to decade variation in stream-flow has been large. Future flow variation will not be significantly different than in the past.
Soil moisture is an important driver of streamflow in the prairies: model predictions of declines in soil moisture in late summer and fall have the potential to decrease streamflow in the spring.
Conclusions: Water Supply Study

## Slide 19
19
Soil moisture is predicted to decrease more towards the later part of the century, most noticeably in the western part of the basin.
Soil moisture is one of the key drivers in generating runoff and stream flow. Higher soil moisture in fall generates higher spring runoff (for example 2011 flood). Future extreme floods may be slightly higher than in the past.
Conclusions: Water Supply Study

## Slide 20
  Questions